ПРИКЛАДНОЕ РУКОВОДСТВО

ПОЛЬЗОВАТЕЛЯ ПРОГРАММНОГО ОБЕСПЕЧЕНИЯ

ЦЕЛЕВАЯ МОДЕЛЬ : AceCop( MDVR-01CH

AceCop( MDVR-01CH

(Mini Mobile DVR-01CH with SD Memory Card)

# REV.RSV1.0.0

(2006 JS TELETEK CO., LTD.

ВСЕ ПРАВА ЗАРЕГИСТРИРОВАННЫ/ ВЫПУСК МАРТ 2006

Головной офис :  10th Fl., ACE Techno Tower III, 197-48,

Kuro-dong, Kuro-gu, Seoul, Korea

Телефон	  :  822-2109-5070(Rep.)

Факс		  :  822-2109-5072

E-mail	  :  jbkim@jsteletek.com

http://www.jsteletek.com

Content

1	INTRODUCTION	3

1.1.	General Description	4

1.2.	Application	3

1.3.	Technical Specification	3

1.4.	Configuration	3

1.5.	Package(Cables and Accessories)	4

2	LAY OUT	6

2.1.	Error Lamp Display	6

2.1.1	Video Loss	6

2.1.2	Memory Error	6

2.2.	NORMAL Lamp Display	6

2.2.1	NORMAL Function	6

3	APPLICATION	7

3.1.	Installation	7

3.1.1	Power	7

3.1.2	Camera Connection	7

3.2.	OSD	7

3.2.1	OSD Connection	7

3.2.2	Remote Controller	7

3.3.	Setup	8

3.3.1	VIDEO-TYPE	9

3.3.2	RESOLUTION	9

3.3.3	REC SPEED	10

3.3.4	REC MODE	10

3.3.5	SENSOR REC TIME	11

3.3.6	FILE SAVING	11

3.3.7	OVERWRITE	12

3.3.8	FORMAT	12

3.3.9	TIME SET	13

3.3.10	EXIT	14

3.4.	BACKUP	15

3.4.1	Connection with PC	15

3.4.2	Viewer Program Installation	16

3.4.3	Viewer Program	19

Introduction

  - General Description

- Though the innovative new technology, MDVR-01CH was designed with the most compact

(pocket/cigarette pack) sized, that makes it easy to record for auto-mobile or anywhere.

The MDVR-01CH stores recorded data or still images from 1CH camera, in SD Memory Card(64M, 512M, 1G, 2G).

- The MDVR-01CH compress the images with MJPEG codec and save them at low capacity with high video quality.

  - Application

- With the MDVR-01CH ‘s compact size and using SD memory cards for storing images, it is the most portable, reasonable and economic solutions for cars, doors in remote locations, the home and etc.

  - Technical Specification

- Operating Temperature : -20º ~ +80º

- Operating Humidity : 0º ~ 80º

| Classification | MDVR-01CH |
| --- | --- |
| Video input | 1CH composite |
| Audio input | No(Option) |
| Display Speed | 20 fps |
| Recording Speed | Max. 15 fps |
| Resolution | 352x288, 720x576 |
| Compression Codec | MJPEG |
| Video Type | PAL/NTSC |
| Memory Type | SD card |
| Back up | USB storage device |
| Overwriting | Available |
| Sensor in / Alarm out | 1 sensor input / 1 alarm output |
| Power | DC 12V, 500mA adaptor |
| Remote control | Available |
| Accessory | USB cable, DC adaptor, Remote controller |

  - Configuration

- Front

- Rear

  - Package(Cables and Accessories)

(1) Cable for Camera in and Camera Power

(2) TV-OUT cable

(3) Remote controller and battery

(4) USB cable

(5) Cigar-jack power cable

(6) DIO cable

Lay Out

  - Error Lamp Display

In case of an error, a red light comes on with a “beep” sound.

    - Video Loss

When there is a “Video Loss”, it beeps 2 times every 10 seconds.

    - Memory Error

If you receive an error while you “Record” or “Delete Memory” it will constantly beep every second.

  - NORMAL Lamp Display

    - NORMAL FUNCTION

| Waiting(Stand-by) Mode |  | Green LED Lighting |
| --- | --- | --- |
| Recording Mode |  | Red LED Lighting |
| USB Backup Mode |  | Green LED Blinking |
| Searching Mode |  | Red LED Blinking |
| Booting Mode |  | Red LED Lighting |

Applicatios

  - Installation

    - Power

MDVR-01CH uses DC 12V power basically.

    - Camera Connection

Camera power connects with provided cable.

  - OSD

    - OSD Connection

You can change selections by inserting RCA cable into both TV-Out

and TV, and also enjoy real-time pictures or use the search function.

    - Remote Controller

  - Setup

Connecting with the TV-monitor it will display live pictures and OSD will show like the picture below.

Press [Menu] button. Then, SETUP menu will be displayed.

Select the menu with the direction key up and down, and change your configuration with the [MENU] button.

When you select your information on the screen it will turn red and the detailed information in white.  At this time you will be able to fix your configuration.

    - Video-Type

Select your video type between ‘NTSC’ and ‘PAL’.

    - RESOLUTION

Select resolution between ‘VGA’ and ‘QVGA’.

* VGA   : 720 x 576

* QVGA  : 360 x 288

    - REC SPEED

Select capture frame rates.

* Selecting Resolution with VGA : 1 / 2 / 5 /10 / 12 FPS

* Selecting Resolution with QVGA : 1 / 2 / 5 / 10 / 15 FPS

    - REC MODE

Select recording mode between “Continuous” and “Sensor”.

    - SENSOR REC TIME

If you select “Sensor REC Time” it will record the way you want it, according to what time you put in.

You may pick from 5 seconds to 20 seconds.  For example if you have your setting; REC SPEED to 15fps, REC MODE to SENSOR REC TIME, and SENSOR REC TIME to 005.   Therefore you will have 75 frames per second altogether.

    - FILE SAVING

There are two ways of saving your recorded data.  One is recording time wise and the other is recording frame wise.

* If you record time wise, you can have : 5 / 10 / 20 / 30 / 60 SEC

For example if you have picked 10SEC it makes a file every 10 seconds all depending on the time.

* If you record frame wise, you pick : 600 FRAME

With the setting 600 FRAME, it make a file when it recorded 600 frames.

    - OVERWRITE

You are given a choice to overwrite or not.

    - FORMAT

To delete the data, you must format the SD memory chip.

Select “FORMAT”

When you receive the message “MEMORY FORMAT? YES/NO” select your command using the direction key up and down

If you select “YES” you will receive a message on the screen “FORMATING…”.

Afterwards, you will return back to the main menu.

    - TIME SET

You may change the time setting of your MDVR-100M using RTC(Real Time Clock) function.

Using the direction keys of the remote control the following time is arrange this way: [ Year-Month-Day Hour:Minute:Second]

When you are done with your arrangements, press [MENU] to exit the configuration.

    - EXIT

Close ‘SETUP’ menu.

  - BACKUP

    - Connection with PC

Make a 1:1 connection from MDVR-01CH to the PC using the USB cable provided.

When the connection is made it will be recognized as a new hardware and also the PC will provide the MDVR-01CH with power supply.

Click [My Computer] and among the files click [Portable Disk] like the picture below.

As you can see in the folder [DCIM], it has a saved file of your recorded movie picture.  They are saved in the order you’ve recorded.  You can play these movie pictures through the program “Viewer”.

If you want to back-up a file, search and copy the file to the folder you wish to put it in.

    - Viewer Program Installation

In order to install the Viewer program on your system, please go to the “MDVRViewer” directory first.

Run ‘Setup.exe’ file to install the viewer program.

Then, Click ‘Next’ to continue installing on your system.

Click “Next” to continue.

Click “Install” to start installing.

Then, click ‘Finish’ to complete installing.

After installing the Viewer program, you will see the above shortcut icon on your desktop screen.

Once you run the Viewer program, it will automatically take you to the Viewer program.

    - Viewer Program

The user runs the short cut icon, he/she will see this viewer program as shown in the above.

Begin : Goes back to the beginning of the movie picture that was playing.

Previous Second : Goes back to the previous frame, frame by frame

Play : Plays the recorded movie picture.

Pause : Pauses the playing movie picture that it was playing

Stop : Stops the playing movie completely

Next Second : Moves on to the next frame, frame by frame

End : Goes to the end of the playing movie picture.

Click “File” and then press “Open”.  There you will be able to select your movie picture.

At the bottom part of the window, you can verify the specific time it was recorded.

Warranty

All AceCop Series products go through various processes and has tough product quality test and they are  subject to a 12 months limited warranty as designed and supplied by JS TELETEK Co., Ltd.’s official distributors.

This warranty does not cover:

- Failure resulting from misuse, accident, modification, unsuitable and improper maintenance by you

- Failure caused by alternation of the parts

- Failure to follow the manual

| Product Name |  |
| --- | --- |
| Product No. |  |
| Warranty period |  |
| Purchase date | Date : |
| Purchaser | Company Name |  |
|  | Name |  |
|  | Address |  |
|  | Phone No. |  |
| Vendor | Company Name |  |
|  | Name |  |
|  | Address |  |
|  | Phone No. |  |

Головной офис :  10th Fl., ACE Techno Tower III, 197-48,

Kuro-dong, Kuro-gu, Seoul, Korea

Телефон	  :  822-2109-5070(Rep.)

Факс		  :  822-2109-5072

E-mail	  :  jbkim@jsteletek.com

http://www.jsteletek.com/

# Text boxes

RESOLUTION       :

4

ON

OVERWRITE        :

VIDEO TYPE        :

10 SEC

SETUP

Time

YY/MM/DD

Record Status (RC/RS)

Record Capacity

Model Name

17 : 10 : 27

Repeat

<Direction Key>

Left, Right Key: Used while searching

Up, Down Key: Used for memory format/time configuration

With the direction key you can search one by one.

2006-02-15

RC

20.5%

Repeat

ON

Mode selection button

3

Remote Control Receiver

Drive selection button

1

005

CONTINUOUS

SENSOR REC TIME  :

REC MODE          :

12FPS

REC SPEED       :

<Menu selection button>

Also used with the ‘ENTER’button.

MDVR-01CH

<Recording>

If the user put this button, status LED is turning on as Red light

When push the button again, LED is changed as Green light. Recording is stooped

<Search>

Pressing this button while its connection to the TV, it will search and also show you recent recorded shows. Pressing it again, you will return to the main menu.

FILE SAVING        :

OVERWRITE        :

FORMAT

PAL

VGA

EXIT

TIME SET

005

CONTINUOUS

SENSOR REC TIME  :

Red light show only when it is recording.

OVERWRITE        :

10 SEC

EXIT

TIME SET

005

CONTINUOUS

SENSOR REC TIME  :

REC MODE          :

ON

OVERWRITE        :

10 SEC

EXIT

TIME SET

005

CONTINUOUS

SENSOR REC TIME  :

ON

OVERWRITE        :

(2)

(1)

10 SEC

EXIT

TIME SET

005

CONTINUOUS

SENSOR REC TIME  :

ON

OVERWRITE        :

10 SEC

EXIT

TIME SET

005

CONTINUOUS

SENSOR REC TIME  :

TIME SET

005

CONTINUOUS

SENSOR REC TIME  :

REC MODE          :

12FPS

REC SPEED         :

VGA

SD memory slot

Drive mode Lamp

5

Normal mode Lamp

Error display Lamp

2

7

6

1

USB port

Power

5

Camera Input

(RJ-12)

4

TV-OUT

3

DIO (RS-232)

2

12FPS

REC SPEED         :

VGA

PAL

FORMAT

ON

OVERWRITE        :

10 SEC

EXIT

TIME SET

005

CONTINUOUS

SENSOR REC TIME  :

REC MODE          :

12FPS

REC SPEED         :

VGA

PAL

FORMAT

REC MODE          :

12FPS

REC SPEED         :

VGA

PAL

FORMAT

ON

OVERWRITE        :

10 SEC

EXIT

TIME SET

005

CONTINUOUS

SENSOR REC TIME  :

REC MODE          :

12FPS

REC SPEED         :

VGA

PAL

FORMAT

ON

OVERWRITE        :

10 SEC

EXIT

TIME SET

005

CONTINUOUS

SENSOR REC TIME  :

REC MODE          :

12FPS

REC SPEED         :

VGA

PAL

FORMAT

REC MODE          :

12FPS

REC SPEED         :

VGA

PAL

FORMAT

REC MODE          :

12FPS

REC SPEED         :

VGA

PAL

FORMAT

REC MODE          :

12FPS

REC SPEED         :

ON

OVERWRITE        :

10 SEC

EXIT

PAL

FORMAT

FILE SAVING        :

RESOLUTION       :

VIDEO TYPE        :

SETUP

TIME SET

EXIT

10 SEC

ON

FILE SAVING        :

RESOLUTION       :

VIDEO TYPE        :

SETUP

FILE SAVING        :

RESOLUTION       :

VIDEO TYPE        :

SETUP

FILE SAVING        :

RESOLUTION       :

VIDEO TYPE        :

SETUP

FILE SAVING        :

RESOLUTION       :

VIDEO TYPE        :

SETUP

FILE SAVING        :

RESOLUTION       :

VIDEO TYPE        :

SETUP

FILE SAVING        :

RESOLUTION       :

VIDEO TYPE        :

SETUP

FILE SAVING        :

RESOLUTION       :

VIDEO TYPE        :

SETUP

ON

OVERWRITE        :

10 SEC

EXIT

TIME SET

005

CONTINUOUS

SENSOR REC TIME  :

REC MODE          :

12FPS

REC SPEED         :

VGA

PAL

FORMAT

FILE SAVING        :

RESOLUTION       :

VIDEO TYPE        :

SETUP

2006-02-10  17 : 10 : 42

VGA

PAL

FORMAT

FILE SAVING        :

RESOLUTION       :

VIDEO TYPE        :

SETUP

MEMORY FORMAT ? YES / NO

FORMATING…

(3)

(4)

(5)

(6)